With high speed PCI V2.1 bus controller and legacy audio SB16® DSPemulator,CMI8738 is designed for PC add-in cards and all-in-one motherboards. No external CODEC is needed in CMI8738: CMI-8738 supports the legacy audio – SB16™, FM emulator/DLS wavetable music synthesis, and HRTF 3D positional audio functions.  Above all CMI8738 supports PCtel® HSP56 (1789) interface.

Being compatible with A3D™ and DirectSound™ 3D, CMI8738 meets PC98® requirements, and supports professional digital audio interface such as 24-bit SPDIF IN (0.5V ~ 5V)and OUT(44.1K and 48K format).

CMI8738 uses HRTF 3D extension technology to enhance traditional HRTF 3D positional audio by substituting two-speaker system by four- speaker one(it supports additional 2CH 16-bit DAC to provide rear side audio).  It greatly improves HRTF 3D positional audio quality and successfully removes the sweet spot limitations: users can enjoy genuine 3D audio gaming effects, and don't have to worry about the environmental confinement any more.

Being outstanding for its full audio functions, competitive price, and power management, CMI-8738 is the best choice for people seeking for optimum use of the PC applications.

C-Media licensed HRTF 3D library from Central Research Lab (CRL®), U.K, who provides one of the world's best HRTF libraries (CRL® also licensed its audio technology to YAMAHA®, ESS®, and other well-known sound chip makers).

#### Features

- HRTF-based 3D positional audio, supporting DirectSound™ 3D and A3D™ interface

- Supports rear side speakers, C3DX positional audio in 4 CH speaker mode

- Legacy audio SB16™ compatible

- DLS-based wavetable music synthesizer, supports DirectMusic™

- Professional digital audio interface supporting 24-bit SPDIF IN and OUT (44.1K and 48K format)

- Built-in 32ohm Earphone buffer

- Built-in PCtel® HSP56 Modem™ interface

- Drivers support AC3® 5.1CH interface.

- MPU-401 port

- Dual game port

- 16-bit full duplex CODEC

- 4 CH 16-bit DAC

- 32-bit PCI bus master

- External E²PROM interface

- Single chip design, +5V, 128 pins QFP

Preliminary         Ver 0.6

CMI-8738/PCI C3DX

PCI-Based HRTF 3D Extension Positional Audio Chip

HSP56 Modem interface

PINOUT

PINOUT

CMI8738/PCI C3DX AUDIO CHIP

QFP 128 PINS

PIN DESCRIPTION

DIGITAL PIN DESCRIPTION

| Name | Number | PIN Type | Definition |
| --- | --- | --- | --- |
| XA31-XA0 | 126-128,1-2,5-7,12-16,19-21,32-35,38-41,43-44,47-52 | I/O | PCI bus address and data lines |
| XINTA | 117 | O | Interrupt request , active-low. |
| XINTB | 118 | O | Modem Interrupt request,active-low |
| XPRST | 119 | I | Reset |
| XCLK33 | 120 | I | PCI bus clock. |
| XGNT | 121 | I | Bus master grant, active-low. |
| XREQ | 122 | O | Bus master request, tri-state output, active-low. |
| XIDSEL | 9 | I | ID select, active-high. |
| XFRAME | 23 | I/O | Cycle frame, active-low. |
| XIRDY | 24 | I/O | Initiator ready, active-low. The bus master device is ready to transmit or receive data |
| XTRDY | 25 | I/O | Target ready, active-low. The target device is ready to transmit or receive data |
| XDEVSEL | 26 | I/O | Device select, active-low. The target device has decoded the address of the current transaction as its own chip select range. |
| XSTOP | 29 | I/O | Stop transaction, active-low. The target device request to the master to stop the current transaction. |
| XPAR | 30 | I/O | Parity. The pin indicates even parity across XA31-XA9 and XCBE3-0 for both address and data phases. |
| XCBE3,2,1,0 | 8,22,31,42 | I/O | Multiplexed command/byte enable. These pins indicate cycle type during the address phase of a transaction. |
| VDD | 4,10,18,27,37,45,54,115,124 | +5V | Digital and PCI I/O power pin |
| GND | 3,11,17,28,36,46,53,116,115 | GND | Digital and PCI I/O ground |
| XIN | 55 | I | 14.318Mhz crystal, or external clock input |
| XOUT | 56 | O | 14.318Mhz crystal |
| XGD7-XGD4 | 97-94 | I | Game port switch input pin. Switch D to switch A |
| XGD3-XGD0 | 93-90 | I/O | Game port resistor input pin. RC3 to RC0 |
| XTXD | 88 | O | MIDI transmit data |
| XRXD | 89 | I | MIDI receive data |
| XSPDIFO | 98 | O | 44.1kHZ SPDIF output |
| XSPDIFI | 86 | I* | 44.1kHZ SPDIF input |
| XSCL | 104 | O | General purpose output |
| XBIO3-XBIO0 | 109-112 | I/O | General purpose I/O |
| VDD5V | 83 | +5V | Digital and PCI I/O power pin |
| VDDM | 100 | +5V | Digital and PCI I/O power pin |
| DGND | 99 | GND | Digital and PCI I/O ground |
| XEECS | 84 | O | EEPROM chip select |

PIN DESCRIPTION

ANALOG PIN DESCRIPTION

| AVDD | 61,81 | +5V | Analog power |
| --- | --- | --- | --- |
| AGND | 60,82 | GND | Analog ground |
| XADOUTL-R | 64,65 | AO1 | Line out |
| XADCHL-R | 66,67 | AI/O | ADC filter |
| XLFILT | 68 | AI/O | Left channel DAC filter |
| XRFILT | 69 | AI/O | Right channel DAC filter |
| XVREF | 63 | AI | Reference Voltage |
| XCDL-R XCDGND | 71,72,70 | AI | CD audio differential input |
| XLNL-R | 75,76 | AI | Line in or Rear speaker out |
| XAUXL-R | 77,78 | AI | Aux. Line in |
| XPCSPKIN | 79 | AI | PC beep signal |
| XMICIN | 80 | AI | Microphone in |
| XREARL-R | 73,74 | AI/O | Rear speaker out |
| XMDSEL | 114 | I | Modes chip select (high:enable) |
| XGPBIO | 87 | O | General purpose I/O pin (0=disabled, 1=enabled) |
| XRING | 101 | I | Ring detection input |
| XOFFHOOK | 102 | O | Off-hook control output |
| XAFERST | 103 | O | Reset signal for MODEM DAA |
| XHSPFS | 105 | O | DAA frame SYNC |
| XHSPSDI | 106 | I | DAA data input |
| XHSPSDO | 107 | O | DAA data output |
| XAFEMCLK | 108 | O | DAA master clock |
| XHNDSET | 113 | O | Reserved |
| XAFEPD | 59 | O | Reserved |
| XMOUT | 58 | O | MODEM crystal output (18.432MHz) |
| XMIN | 57 | I | MODEM crystal input |
| XMBCSZ | 85 | I | Audio chip select (low:enable) |

| Name | Number | Definition |
| --- | --- | --- |
| XTXD | 88 | When pull-down select add-on mode, default pull-high motherboard. |
| XAFEPD | 59 | When pull-down enable #INTB share with #INTA, default high disabled. |
| XHNDSET | 113 | When pull-down enable external 18.432Mhz x'tal to HSP module, default pull-high enable internal 24.576Mhz to HSP module. |
| XBIO0 | 112 | When pull-down select CLKGEN ref. clock to external 24.576Mhz x'tal. default pull-high select 14.318Mhz |

ELECTRICAL CHARACTERISTICS

Absolute Maximum Ratings

| Ratings | Symbol | Value | Units |
| --- | --- | --- | --- |
| Digital power voltage | VDD | VDD(5% | V |
| Analog power voltage | AVDD | AVDD(5% | V |
| Operating temperature range | TO | 0 to 70 | (C |
| Storage temperature range | TST | -40 to 125 | (C |
| Maximum power dissipation | PDMAX | 300 | MW |

Digital Characteristics

| PARAMETER | Symbol | Min | Typ | Max | Unit |
| --- | --- | --- | --- | --- | --- |
| Input high voltage(PCI I/O) | VIH | 2. |  | VDD+0.5 | V |
| Input low voltage (PCI I/O) | VIL | -0.5 |  | 0.8 | V |
| Output high voltage | VOH | 2.4 |  | VDD | V |
| Output low voltage | VOL | 0.0 | 0.2 | 0.4 | V |
| SPDIF IN input high voltage | VIH1 |  | 2.6 |  | V |
| SPDIF IN input low voltage | VIL1 |  | 2.4 |  | V |
| SPDIF output high voltage | VOH1 |  | VDD |  | V |
| SPDIF output low voltage | VOL1 |  | VSS |  | V |
| Output buffer current |  |  | 5 |  | mA |

Audio Characteristics

| PARAMETER | Symbol | Min | Typ | Max | Unit |
| --- | --- | --- | --- | --- | --- |
| Analog input voltage | Avin |  | 1.1 |  | VRms |
| Analog output voltage | Avout |  | 1.1 |  | VRms |
| A-A S/N ratio |  |  | 85 |  | db |
| A-A THD |  |  | 0.09 |  |  |
| ADC S/N ratio |  |  | 80 |  | db |
| ADC THD |  |  | 0.1 | 0.2 | % |
| DAC S/N ratio |  |  | 80 |  | db |
| DAC THD |  |  | 0.1 | 0.2 | % |
| SPDIF IN/OUT S/N ratio |  |  | 120 |  | db |
| SPDIF IN/OUT THD |  |  | 0 |  | % |
| Microphone input level |  | 20 |  | 200 | mv |
| Microphone booster |  |  |  | 20 | db |

Application circuit: (for mainboard purpose)

BOM: (for mainboard)

| No. | Quantity | Reference | Part |
| --- | --- | --- | --- |
| 1 | 4 | C1,C13,C17,C19 | 101 |
| 2 | 28 | C2,C3,C5,C6,C7,C8,C9,C11, | 104 |
|  |  | C12,C23,C26,C27,C36,C37, |  |
|  |  | C38,C41,C42,C43,C48,C49, |  |
|  |  | C50,C51,C52,C55,C56,C59, |  |
|  |  | C60,C61 |  |
| 3 | 5 | C4,C14,C44,C53,C54 | 10UF/16V |
| 4 | 1 | C10 | 1UF/16V |
| 5 | 9 | C15,C21,C25,C29,C30,C31, | 102 |
|  |  | C39,C46,C47 |  |
| 6 | 1 | C16 | 224 |
| 7 | 2 | C18,C22 | 470UF/16V |
| 8 | 2 | C20,C24 | 270 |
| 9 | 2 | C28,C34 | 20PF |
| 10 | 4 | C32,C35,C40,C45 | 822 |
| 11 | 2 | C57,C58 | (20PF) |
| 12 | 1 | D1 | 1N4148 |
| 13 | 1 | D2 | ZERNER1/3.6V |
| 14 | 1 | GAME1 | DB2F15 |
| 15 | 2 | J2,J3 | PIN 1X4 |
| 16 | 1 | J4 | PIN 1X3 |
| 17 | 1 | J5 | CD-JACK/PANASONIC |
| 18 | 1 | J6 | PIN 1X2 |
| 19 | 1 | JP1 | PIN 2X8 |
| 20 | 4 | L1,L2,L3,L4 | 201209U280 |
| 21 | 3 | LINE1,MIC1,SPK1 | PHONEJACK3P |
| 22 | 1 | Q1 | 78L05 |
| 23 | 1 | Q2 | 2N3904/NA |
| 24 | 10 | R2,R3,R4,R5,R6,R7,R13, | 10K |
|  |  | R15,R36,R41 |  |
| 25 | 2 | R8,R10 | 4.7K |
| 26 | 1 | R9 | 100 |
| 27 | 2 | R11,R12 | 1K |
| 28 | 2 | R16,R34 | OPEN(10K) |
| 29 | 4 | R17,R27,R42,R45 | 0 |

| No. | Quantity | Reference | Part |
| --- | --- | --- | --- |
| 30 | 1 | R18 | OPEN(33) |
| 31 | 1 | R19 | 47 |
| 32 | 4 | R23,R24,R26,R30 | 2.2K |
| 33 | 2 | R25,R38 | 560 |
| 34 | 1 | R29 | 10 |
| 35 | 1 | R32 | OPEN(1OK) |
| 36 | 1 | R33 | 1(0805)or bead core(0805) |
| 37 | 1 | R35 | 10K(OPEN) |
| 38 | 2 | R37,R44 | 75 |
| 39 | 1 | R39 | 1M |
| 40 | 3 | R40,R41,R43 | 10K/NA |
| 41 | 2 | SLOT1,SLOT2 | --- |
| 42 | 1 | SPDIFOUT1 | RCA JACK |
| 43 | 5 | TP1,TP4,TP5,TP6,TP9 | TEST PIN |
| 44 | 1 | U1 | CMI8738 |
| 45 | 1 | U2 | 93C46 |
| 46 | 1 | Y1 | 14.318MHZ |
| 47 | 1 | Y2 | (18.432MHZ) |

Application circuit: (for add-on card purpose)

BOM: (for add-on card)

| No. | Quantity | Reference | Part |
| --- | --- | --- | --- |
| 1 | 7 | C1,C5,C21,C24,C51,C62, | 10UF/16V |
|  |  | C63 |  |
| 2 | 6 | C2,C6,C18,C19,C22,C23 | 101 |
| 3 | 28 | C3,C4,C8,C9,C11,C13,C14, | 104 |
|  |  | C15,C16,C30,C31,C32,C33, |  |
|  |  | C34,C35,C42,C43,C44,C45, |  |
|  |  | C50,C52,C53,C57,C58,C59, |  |
|  |  | C60,C61,C64 |  |
| 4 | 1 | C7 | 224 |
| 5 | 1 | C10 | 1UF/16V |
| 6 | 9 | C12,C26,C29,C36,C37,C38, | 102 |
|  |  | C47,C55,C56 |  |
| 7 | 2 | C17,C20 | 470UF/16V |
| 8 | 2 | C25,C28 | 270 |
| 9 | 2 | C27,C40 | (20PF) |
| 10 | 4 | C39,C41,C48,C54 | 822 |
| 11 | 2 | C46,C49 | 20PF |
| 12 | 1 | CN1 | PIN 2X5 |
| 13 | 1 | CN2 | PIN 2X8 |
| 14 | 1 | D1 | 3.6V(modem only) |
| 15 | 1 | GAME | DB2F15 |
| 16 | 2 | J1,J4 | PIN 1X2 |
| 17 | 2 | J2,J3 | PIN 1X4 |
| 18 | 1 | J5 | CD-JACK/PANASONIC |
| 19 | 4 | L1,L2,L3,L4 | 201209U280 |
| 20 | 4 | LINE,MIC,REAR,SPK | 3.5 PHONE JACK |
| 21 | 1 | Q1 | 78L05 |
| 22 | 10 | R1,R2,R3,R4,R6,R7,R8,R11 | 10K |
|  |  | R13,R14 |  |
| 23 | 1 | R5 | 100 |
| 24 | 2 | R9,R10 | 1K |
| 25 | 1 | R12 | 75 |

| No. | Quantity | Reference | Part |
| --- | --- | --- | --- |
| 26 | 2 | R15,R28 | 560 |
| 27 | 3 | R16,R19,R25 | OPEN(10K) |
| 28 | 1 | R17 | 47 |
| 29 | 1 | R18 | 1M |
| 30 | 4 | R20,R27,R30,R32 | 2.2K |
| 31 | 5 | R21,R24,R29,R31,R38 | 0 |
| 32 | 2 | R22,R23 | OPEN |
| 33 | 1 | R26 | 10K(OPEN) |
| 34 | 1 | R33 | 10(OPEN) |
| 35 | 2 | R34,R37 | OPEN(0) |
| 36 | 1 | R35 | 1(0805)or bead core(0805) |
| 37 | 1 | R36 | 75(modem only) |
| 38 | 1 | SLOT1 | PCIC2 |
| 39 | 1 | SLOT2 | PCIS2 |
| 40 | 1 | SPDIFOUT | RCA JACK |
| 41 | 4 | TP1,TP2,TP3,TP9 | TEST PIN |
| 42 | 1 | U1 | 93C46 |
| 43 | 1 | U2 | CMI8738 |
| 44 | 1 | Y1 | (18.432MHZ) |
| 45 | 1 | Y2 | 14.318MHZ |

Application circuit: (SPDIF optical module)

BOM: (for SPDIF optical module)

| No. | Quantity | Reference | Part |
| --- | --- | --- | --- |
| 1 | 5 | C1,C2,C4,C5,C6 | 104 |
| 2 | 1 | C3 | 10UF/16V |
| 3 | 1 | CN1 | PIN 2X5 |
| 4 | 1 | J1 | PIN 1X2 |
| 5 | 1 | L1 | 47UH |
| 6 | 1 | Q1 | 78L05 |
| 7 | 2 | R1,R2 | 4.7K |
| 8 | 1 | SPDIFIN | TORX178A |
| 9 | 1 | SPDIFOUT | TOTX178 |

Configuration

CMI8738 PCI Configuration Spaces(Audio)

00h	13F6 : (Vender ID) read only

02h	0111 : (Device ID) read only

04h 0006 : Command  (State after #RST all is “0”)

0 (bit 9) Fast back-to-back enable

0 (bit 8) #SERR enable (R/W)

0 (bit 7) Wait cycle control

0 (bit 6) Parity error response

0 (bit 5) VGA palette snoop

0 (bit 4) Memory write and invalidate enable

0 (bit 3) Special cycles

1 (bit 2) Bus master (R/W)

0 (bit 1) Memory space

1 (bit 0) I/O space (R/W)

06h 0280 : Status

0 (bit 15) Detected Parity Error

0 (bit 14) Signaled System Error

0 (bit 13) Received Master Abort

0 (bit 12) Received Target Abort

0 (bit 11) Signaled Target Abort

01 (bits 10-9) DEVSEL timing 00-fast, 01-medium, 10-slow

0 (bit 8) Data Parity Error Detected

1 (bit 7) Fast Back-to-Back Capable

0 (bit 6) UDF Supported

0 (bit 5) 0-33MHz ,1-66MHZ Capable

00000 (bits 4-0) Reserved

08h 10 : Revision ID

09h 040100 : Audio device

0Ch 00 : Cache Line Size

0Dh 20 : Latency Timer

0Eh 80 : Header Type

0Fh 00 : BIST

10h 0000d401 : I/O of length : -65280(ffff0100h) : First Base Address register

14h 00000000 : Uninitialized : Second Base Address register

Configuration

18h 00000000 : Uninitialized : Third Base Address register

1Ch 00000000 : Uninitialized : Fourth Base Address register

20h 00000000 : Uninitialized : Fifth Base Address register

24h 00000000 : Uninitialized : Sixth Base Address register

28h 00000000 : Cardbus CIS Pointer

2Ch 13f6 : (SubSystem Vender ID) (R/W)

2Eh ffff : SubSystem ID (R/W)

30h 00000000 : Expansion ROM Base Address

34h 00000000 : Reserved

38h 00000000 : Reserved

3Ch 05 : Interrupt Line

3Dh 01 : Interrupt Pin

3Eh 02 : Min Grant

3Fh 18 : Max Latency

CMI8738 Configuration Spaces(Modem)

00h 13F6: (Vender ID) read only

02h 0211: (Device ID) read only

04h Command (State after #RST all is "0")

0 (bit 9) Fast back-to-back enable (read only)

0 (bit 8) #SERR enable (Read only)

0 (bit 7) Wait cycle control (read only)

0 (bit 6) Parity error response (read only)

0 (bit 5) VGA palette snoop (read only)

0 (bit 4) Memory write and invalidate enable (read only)

0 (bit 3) Special cycles (read only)

0 (bit 2) Bus master (read only)

1 (bit 1) Memory space (R/W)

0 (bit 0) I/O space (read only)

06h Status

B0 (bit 15) Detected Parity Error

B0 (bit 14) Signaled System Error

B0 (bit 13) Received Master Abort

B0 (bit 12) Received Target Abort

B0 (bit 11) Signaled Target Abort

B01 (bits 10-9) DEVSEL timing 00-fast, 01-medium, 10-slow

B0 (bit 8) Data parity Error Detected

B0 (bit 7) Fast Back-to-Back Capable

B0 (bit 6) UDF Supported

B0 (bit 5) 0-33MHz, 1-66MHz Capable

B00000 (bits 4-0) Reserved

08h X10: Revision ID

09h X078000: Communication device (Modem)

0Ch X00: Cache Line Size

0Dh X00: latency Timer

oEh X80: Header Type (Multifunction device)

oFh X00: BIST
10h Xbbbbb000: Allocate 4K memory space.

14h X00000000: not used - Second Base Address register

18h X00000000: not used - Third Base Address register

1Ch X00000000: not used- Four Base Address register

20h X00000000: not used- Fifth Base Address register

24h X00000000: not used- Sixth Base Address register

28h X00000000: Card bus CIS Pointer

2Ch X13f6: Sub-System Vender ID (Value can be replaced after reset.) (R/W)

2Eh X0211: Sub-System ID (Value can be replaced after reset) (R/W)

*Refer to the Audio PCI registers bit-13 of address (18-1B) for how to replace.30h X00000000: Expansion ROM Base Address

34h X00000040: pointer to the power-saving registers. (Read only)

38h X00000000: Reserved

3Ch X00: Interrupt Line (R/W)

3Dh Interrupt Pin(X01 share interrupt/X02 not share interrupt with Audio)

*Select from the power on pin configuration

3Eh X00: Min Grant(not used)

3Fh X00: max Latency(not used)

40h XEC4A0001(read only)

44h-47h

B0-B1: PMST (R/W) (11)

B7-B2: all 0 (read only)

B8: PMEEN (R/W) (Sticky bit)

B12-B9: DSEL (R/W) 0000

B14-B13: all 0 (read only)

B15: PMESTS (Sticky bit)

DMA Slave Configuration Register(R/W)	     PCI Configuration address 40H

Configuration

Bit(s)	Function

31:16	Reserved

15:4	Slave Base Address 15-4. INTEL VX chipset seleted if Base Address 15:4=000h

3	Non legacy Extended Addressing

- =  disabled

- =  enabled

2:1	Transfer Size

00  =	 8 bit transfer

- =  16 bit transfer

- =  32 bit transfer, non legacy

- =  Reserved

- Channel Enable

- =  disabled

- =  enabled

Internal Register Mapping

##### Function Control Register 0

Address	00H

Bit(s)		R/W		Name		Description

31:20				Reserved.

19				RST_CH1		Channel1,	1->Reset	(Default 0)

18				RST_CH0		Channel0,	1->Reset	(Default 0)

17				CHEN1		Channel1,	1->Enabled,		0->Disabled.

16				CHEN0		Channel0,	1->Enabled,		0->Disabled.

15-2				Reserved

3				PAUSE1		Channel1, 	1->Pause if channel1 is enabled.

2				PAUSE0 		Channel0,	1->Pause if channel0 is enabled.

1				CHADC1		Channel 1 , 1->Recording, 	0->Playback

0				CHADC0		Channel 0, 	1->Recording,	0->Playback

##### Function Control Register 1

Address	04H

Bit(s)		R/W		Name		Description

31-16				Reserved

15:13 			DSFC[2:0]		DAC Sampling Frequency Select,

0	0	0	5.512 K

0	0	1	11.025 K

0	1	0	22.05 K

0	1	1	44.1 K

1	0	0	8 K

1	0	1	16 K

1	1	0	32 K

1	1	1	48 K

12:10			ASFC[2:0]		ADC Sampling Frequency Select,

0	0	0	5.512 K

0	0	1	11.025 K

0	1	0	22.05 K

0	1	1	44.1 K

1	0	0	8 K

1	0	1	16 K

1	1	0	32 K

1	1	1	48 K

9				SPDF_1		SPDIF IN/OUT at Channel B at 44.1K double-words/sec.

8				SPDF_0		SPDIF OUT only at Channel A at 44.1K double-words/sec.

7				SPDFLOOP	external SPDIF/IN loopback to external SPDIF/OUT .

6				SPDO2DAC	SPDIF/OUT can be heard from internal DAC.

5				INTRM		Interrupt Mask bit for MCB (Master control block) module interrupt.

0	MCB interrupt disabled.

1	MCB interrupt enabled.

4	 BREQ	If this bit is set low it will prevent the MCB and DAC/ADC block from accessing the memory.

0	Bus Master request disabled(power on state)

1	Bus Master request enabled.

3				VOICE_EN		This bit enables Legacy Voice device(SB16,FM).

0	Legacy Voice disabled on channel 0.

1	Legacy Voice enabled on channel 0.

2				UART_EN		This bit enables Legacy UART device.

0	UART disabled

1	UART enabled

1				JYSTK_EN 	This bit enables Legacy Joystick device.

0	Joystick disabled

1	Joystick enabled

0							Reserved

Channel Format Register

Address	08H

Bit(s)		R/W		Name		Description

31:16				Reserved

15-14	AdcBitLen[1:0]	Sample resolution

- 16 Bits per sample . (Default)

- 15 Bits per sample.

- 14 Bits per sample.

- 13 Bits per sample.

13-12	AdcDacLen[1:0]	Sample resolution

- 600nSec per bit in a sample.

- 660nSec per bit in a sample.

- 1.3uSec per bit in a sample. (Default)

- 2.8uSec per bit in a sample.

11				CH1 Ssmple Rate 176K

10				CH1 Sample Rate 88K

9				CH0 Sample Rate 176K

8				CH0 Sample Rate 88K

7:4				reserved

3:2				CH1FMT[1:0]	Data format of channel 1

00	8 bit	Mono mode

01	8 bit	Stereo mode

10	16 bit	Mono mode

11	16 bit	Stereo mode

1:0				CH0FMT[1:0]	Data format of channel0

00	8 bit	Mono mode

01	8 bit	Stereo mode

10	16bit	Mono mode

11	16 bit	Stereo mode

Interrupt Hold/Clear Register

Address	0CH

Bit(s)		R/W		Name		Description

31:19				Reserved

18				TDMA_INT_EN	Interrupt hold/clear bits for updating TDMA position

- Interruupt Clear

- Interrupt Hold if exist.

17				CH1_INT_EN	Interrupt hold/clear bits for the Channel 1.

- Interrupt Clear

- Interrupt Hold if exist.

16				CH0_INT_EN	Interrupt hold/clear bits for the Channel 0.

0				Interrupt Clear

1				Interrupt Hold if exist.

15:0				Reserved

Interrupt Register

Address	10H

Bit(s)		R/W		Name		Description

31		R		INTR			Interrupt reflected from any sources.

- No interrupt

- Interrupt pending

30:28				Reserved

27		R		VCO

26		R		MCBint		Abort conditions occur during PCI Bus Target/Master Access.

0	No interrupt

- Interrupt pending

25:17				Reserved

16		R		UARTint		This bit is the UART interrupt bit.

- No UART interrupt

- UART interrupt pending

15:		R		LTDMAINT		Interrupt for updating Low Channel TDMA position.

- No interrupt

1	Interrupt pending

14		R		HTDMAINT		Interrupt for updation High Channel TDMA position.

- No interrupt.

1	Interrupt pending.

13:8				Reserved

7		R		XDO46		Direct programming EEPROM interface , read data register

6		R		LHBTOG		High/Low status from DMA CTRL register.

5		R		LegHDMA		Legacy is in High DMA channel.

4		R		LegStereo		Legacy is in Stereo mode.

3		R		Ch1Busy		Channel B Busy.

2		R		Ch0Busy		Channel A Busy.

1		R		Chint1		Channel B Interrupt.

- No interrupt

- Interrupt pending

0		R		Chint0		Channel A Interrupt.

0	No interrupt

1	Interrupt pending

Legacy Control/Status Register

Address	14H

Bit(s)		R/W		Name		Description

31				Reserved

30:29				VMPU [1:0]	Base address for MPU401 access

- Base address : 330h

- Base address : 320h

10	Base address : 310h

11	Base address : 300h

- Reserved

27:26				VSBSEL[1:0]	The Base Address Select for SB16 access.

- Base address: 220h

- Base address: 240h

- Base address: 260h

- Base address: 280h

25:24				FMSEL[1:0] 	The Base Address Select for FM access.

- Base address : 388h

- Base address : 3C8h

- Base address : 3E0h

- Base address : 3E8h

- ENSPDOUT	enable  XSPDIF/OUT  to  I/O Interface

- SPDCOPYRHT  SPDIF IN/OUT  CopyRight status bit

- DAC2SPDO	enable Wave+FM+MIDI to SPDIF/OUT interface

20				SetRetry		Mode of wait state .  0:legacy I/O wait (default) 1:legacy I/O BUS retry

- C_EEACCESS  Direct programming EEPROM interface Registers.

- C_EECS

- C_EEDI46

- C_EECK46

15-0	Reserved

Micellaneous Control Register

Address	18H

Bit(s)		R/W		Name			Description

31				PWD			Power Down Mode enabled..

30				RESET		Reset Bus Master/DSP Engine.

29:28				SFIL[1:0]		Four level of filter control at the front end DAC..

27				TX/VX		Which motherboard to work with

- VX chip sets.

- TX chip sets.

26				N4SPK3D

25				SPDO5V

24				W / SPDIF48K ; R / SPATUS48K ;

23				ENDBDAC	Default low, High will enable Double DAC structure.

22				XCHGDAC	Default low,

0	CH0 > Front SPKR,	CH1 > Back SPKR.

1	CH0 > Back SPKR,	CH1 > Front SPKR.

21				SPD32SEL		when high, support 32bits SPDIF format ,low 16bits

20				SPDFLOOPI	internal SPDIF/OUT loopback to internal SPDIF/IN, for loopback testing

19				FM_EN		Legacy FM enabled.

18				Reserved

17				Reserved

16				VIDWPDSB	Sub ID write protect disabled. (default 0)

15				SPDF_AC97    0: SPDIF/OUT 44.1K  1:SPDIF/OUT 48K(share with AC97 transfer)

14				MASK_EN		Activate channel mask on Legacy DMA.

- Disabled

- Enabled

13				VIDWPDSB	Write Protect of HSP Configuration Sub ID.

- Protect.

- No protect.

12				SFILENB		Let software contrl filter stepping at the front end DAC.

11-9				Mmode[2:0]     Modem DAA interface mode selection,default 000

000 	Modem in Local DAA interface mode

001  Modem in AC97_LINK mode

010	Modem in parallel CM_LINK mode (external modem bridge supported)

1XX	Modem in serial CM_LINK mode (external modem bridge supported)

8				Reserved

7				FLINKON		force Link detection on when in CM_LINK mode,default 0

6				FLINKOFF		force Link detection off when in CM_LINK mode,default 0

5				Reserved

4				MIDSMP		Enable 1/2 interpolation at the Front end DAC..

3:2				UPDDMA[1:0]	For every the number of samples to notify updating TDMA position.

- Every 2048 samples

- Every 1024 samples

- Every 512 samples.

- Every 256 samples.

1:0				TWAIT[1:0]	For controling the length of legacy BUS cycle.

- 3 PCICLK.

- 18 PCICLK.

- 24 PCICLK

- 32 PCICLK

* Notice	REQ_SQ[2:0]			States of BusRequest Engine.

MM_DATA			Bus Master  is using Bus.

MIDLE				Bus Master is not using Bus.

REQA/REQB			Channel 0/1 BusMaster Request.

GNTA/GNTB			Channel 0/1 BusMaster Grant.

ADRQ/BDRQ			Channel 0/1 DMA  Request.

ADACK/BDACK		Channel 0/1 DMA  Acknoledge.

AIRQ/BIRQ			Channel 0/1 Interrupt.

CX/BX				Channel 0/1 Busy.

Mixer Control / Device Configure Register (can be accessed only by BYTE instruction)

Address	20H

Bit(s)		R/W		Name			Description

7:0		W		SBVR[7:0]		Programmable SB16 version No.

R		DEV[7:0]		Hardwire device version No.

Address	21H

Bit(s)		R/W		Name			Description

7							Reserved

6							Reserved

5:4							Reserved

3							Reserved

2				X_ADPCM		SB16  ADPCM enable,default disabled.

1				PROINV		SBPro Left/Right channel switching.

0				X_SB16		Indicate device active as SB16 compatible, default SB16

Address	22H

Bit(s)		R/W		Name			Description

7:0				IDXdata		Mapping SB16 mixer INDEX register data port(A2x5h)

Address	23H

Bit(s)		R/W		Name			Description

7:0				IDXaddr		Mapping SB16 mixer INDEX register address port(A2x4h)

Address	24H

Bit(s)		R/W		Name		Description

7				Fmmute		Mute FM

6				Wsmute		Mute Wave stream

5				SPK4		select four speaker mode(emulate Line in to Line out )

4				Rear2front		exchange rear and front channels’s speaker out

3				Waveinl		Digital Wave recording Left channel

2				Waveinr		Digital Wave recording Right channel

1				X3DEN		3D surround enable.

0				Cdplay		SPDIF/IN PCM to DAC enable

Address	25H

Bit(s)		R/W		Name			Description

7				RAUXREN	Recording source select R-Aux

6				RAUXLEN		Recording source select L_Aux

5				VAUXRM		R-AUX mute control

4				VAUXLM		L-AUX mute control

3:1				VADMIC[2:0]	Recording MIC volume control

0				MICGAINZ	MIC gain control,default high

Address	26H

Bit(s)		R/W		Name			Description

7:4				VAUXL[3:0]	L-AUX volume control

3:0				VAUXR[3:0]	R-AUX volume control

Address	27H

Bit(s)		R/W		Name			Description

0				DMAUTO		SB16 Low/High DMA  Auto detect enabled ,When high.

1				SPDVALID	SPDIF/IN valid bit detect enabled, When high.

2				XGPBIO		general purpose bi-direction pin, when high output tri-state

3							Reserved

4							Reserved

5				XGPO1		general purpose output pin 1,this pin shared with XSPDIFO pin, and enabled when index reg. F0_bit 0 programmed high.

6:7							Reserved

Mup401  PCI Port

Index address	40-4FH

FM  PCI Port

Index address	50-5FH

##### Legacy SB16 mixer

| Index | D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 0x00 | Reserved |
| 0x04 | Wave volume left channel | Wave volume right channel |
| 0x0A |  | Mic volume |
| 0x22 | Master volume left channel | Master volume right channel |
| 0x26 | FM volume left channel | FM volume right channel |
| 0x28 | Analog-CD volume left channel | Analog-CD volume right channel |
| 0x2E | Line-in volume left channel | Line-in volume right channel |
| 0x30 | Reserved |
| 0x31 | Reserved |
| 0x32 | Reserved |
| 0x33 | Reserved |
| 0x34 | Reserved |
| 0x35 | Reserved |
| 0x36 | Reserved |
| 0x37 | Reserved |
| 0x38 | Reserved |
| 0x39 | Reserved |
| 0x3A | Reserved |
| 0x3B | PC spk volume |  |  |  |  |  |  |
| 0x3C |  | Output muting controls |
|  |  | Line L | Line R | CD L | CD R | Mic |
| 0x3D |  | Recording left channel controls |
|  |  | FM L | FM R | Line L | Line R | CD L | CD R | Mic |
| 0x3E |  | Recording right channel controls |
|  |  | FM L | FM R | Line L | Line R | CD L | CD R | Mic |
| 0x3F | Reserved |
| 0x40 | Reserved |
| 0x41 | Reserved |
| 0x42 | Reserved |
| 0x43 | Reserved |
| 0x44 | Reserved |
| 0x45 | Reserved |
| 0x46 | Reserved |
| 0x47 | Reserved |
| 0x80 |  | IRQ channel (read only) |
|  |  | IRQ10 | IRQ7 | IRQ5 | IRQ2(9) |
| 0x81 | 16 bit DMA channel (read only) | 8 bit DMA channel (read only) |
|  | DMA 7 |  | DMA 5 |  | DMA 3 |  | DMA 1 | DMA 0 |
| 0x82 |  | Interrupt status (read only) |
|  |  | MPU-401 | 16bit DMA | 8bit DMA |

* Please do not write any values into reserved registers

CMI8738 SPDIF IN/OUT Test Report

- SPDIF OUT (playback) > 120db

- SPDIF IN (recording ) > 120db

- SPDIF through mode (bypass) > 120db

* This report is generated by Audio Precision® System II using multi-tone mode.

- Stereo

It is only one-dimensional, as sounds come from (left /right) the physical location of speakers.

- Surround (Stereo Expander )

It filters the existing stereo signal to make the sounds fill in the area around the speakers, and in front of the listener.  Sound sources appear to come from outside the physical locations of the speakers.

- Multi-Speaker Surround (Dolby Pro Logic or Digital AC-3)

It uses five speakers instead of two to surround the listener; hence, sound sources come from five directions and create engaging audio experience.  This surround sound effect, however, has to be pre-recorded, and it dose not support interactive environment.

- HRTF 3D Positional 3D (C-Media 3D)

Only this sound processing technology can be called real 3D manifestation, as 3D usually refers to the three dimensions of X, Y and Z.  This technology allows people to pin-point the location of sound in the real world (up/down, left/right, front/back)using only two speakers or a pair of headphones.  This technology also supports interactive 3D applications to get a real-time placement of sounds via API (application programming interface) such as Microsoft DirectSound3DTM.  We can also use this technology to simulate Multi-speaker Surround with two physical speakers to deliver five “virtual" speakers in the air, surrounding the listener and creating home theater sound environment.  This is the most economical and the easiest solution to people who would like to get high performance surround sound but don’t want to spend money in adding extra speakers.

- HRTF 3D Extension Positional (C-Media 3DX)

3D illusion exists because traditional 3D positional audio system assumes the user's position as the sweet spot to design crosstalk-cancellation circuit; therefore, if the user wants to have 3D positional audio effects, he can’t move his head or position out of sweet spot.   Another 3D illusion fails because half the population are compulsive "head-turners" who will never get 3D audio from two speakers .  To remedy this, C-Media utilizes HRTF 3D extension technology (C3DX) to enhance traditional HRTF 3D positional audio by substituting two-speaker system by four-speaker one.  Therefore, at least one or two speakers should be placed  behind the listener's head to complement the rear-side effect, thus creating compelling realistic sound.  This technology greatly improves HRTF 3D positional audio quality, and successfully eliminates the sweet spot limitation. Users can enjoy the real 3D audio gaming effects, and don't have to worry about the environmental confinement any more.

C3D HRTF Positional Audio Technology

C3D technology uses an audio filter called Head Related Transfer Functions (HRTFs), which is licensed from CRL®(Central Research Lab).  The basic concept of C3D is: since we can hear sound three dimensionally in the real world using our two ears, it must be possible to regenerate the same sound effect from two loud speakers.

What is HRTF ?

HRTF (Head Related Transfer Functions) is a set of audio filters which can vary locations of sound effects (spatial hearing cues) in three-dimension measured from the listener's eardrum.

People can use this technology and special digital signal processing to re-create spatial hearing cues, so as to makes the ears hear a realistic and three-dimensional sounds coming from a pairs of loud speakers or headphones.

There are several listening cues which allow people to hear sounds three-dimensionally :

(I).   Spatial Hearing : Primary 3D-cues

1.	IAD

The head shadowing effect creates differences in the amplitudes of the sound signals arriving at each ear from the source.  The effects of diffraction are most noticeable in the range between about 700 Hz to 8 KHz, where the A and S functions periodically converge and diverge gently.  This Inter-aural Amplitude difference (IAD) is one of the primary 3D sound cues.

2.	ITD

In addition to IAD, there is also a time-of-arrival difference between the left and right ears(unless the sound source is in one of the pole positions, such as  directly in front, behind, above and below): this is known as the Inter-aural Time Delay (ITD).

3.	Pinna Effects

It has been presumed by several researchers that the convolutions of the pinna create the spectral features which constitute the 'height' cues.  In practical experiments by Gardner, in which different parts of the pinna were occluded, and then the ability of a number of subjects to identify sound source positions at different heights was tested, it was shown that the different features all contributed by different amounts.  For example, if the fossa is excluded, then height localization capability is impaired, but not totally extinguished.  It would be reasonable to conclude that it is the combined effect of the pinna convolutions which create the various localization cues, and it is not valid - or logical - to attempt to assign particular spatial capabilities with individual physical features.

(II).  Spatial Hearing : Secondary 3D-cues (shoulder & local reflections)

In addition to the 'primary' 3D sound cues (IAD, ITD and pinna effects), there are several additional cues which do contribute to the localization capability; these will be referred to here as 'secondary' cues, and include shoulder/torso reflections, local room reflections, and psychological cues.

1.	Shoulder / Torso reflections

The presence of a torso attached to an artificial head has the effect of increasing the pressure in the vicinity of the ear up to frequencies of around 2 kHz.  The effect is greater for frontal sources than lateral ones.  In experience, the presence of the torso does not appear to contribute much to spatial accuracy.  However, shoulders are located very close to the ears, and their effect is greater, this time, in respect of

lateral sounds.  If one listens to an artificial head first without - and then with - shoulder fitments, then it is clear that the shoulders do contribute to spatial effects in certain positions.  The shoulders provide a strong reflection from lateral sources, with a short path-length of around 10 cm between direct sound and reflection.  The effects are most important for side-positioned sources, especially for "height" effects, where the shoulders tend to mask sources which move below about 30 degree depression.

- Local, Room Reflections

In simulations, it is clear that the incorporation of first-order simulated room reflections can help in the creation of sound images which have a "solid" nature.  However, the effects - if accurately simulated - are relatively slight.  Experience has shown that it is primarily the quality of the HRTFs themselves which determine the quality and solidity of the sound image.  The further addition of second-order reflections does not help significantly, because in reality, there is a great number of reflections in the average room.  A method which does help to recreate the acoustic experience of a room, however, is to use approximate simulations of lateral reverb, using either 2 or 4 laterally placed "virtual" sources at, say, +-70 degrees and 80 degrees azimuth.

- The quality of the sound image relates to the HRTFs used.

- The quality of the room image relates to addition of reflections and reverb.

3. Psychological Cues

There are clearly psychological cues present in everyday life which work together with the audio cues to tell us about the world around us.  For example, if you hear the sound of a helicopter flying, you expect it to be up in the air, and not downwards.  If a dog is barking nearby, you would expect it to be downwards.

How to listen to C3D sound correctly and properly?

1.	Use Headphones to Have Much Better Effect

When you use headphones in listening, there will be less interference such as outside voices or room reflections comparing to using speakers.

2.	Choose Correct Output Devices

Choose the correct output devices in the options of demo program in accordance with what listening devices you want to listen to.  Listening through speakers must be proceeded by crosstalk-cancellation, so if you choose the wrong output devices, there won’t be any 3D positional audio effect.

3.	Position of Speakers

If you listen from speakers, please do not reverse the left and right speakers, which  should be put in equal distance from the listener.  That is, the listener, the left, and the right speaker must be in the topmost of a right triangle. The position of the listener is called the “sweet spot”. In addition, the height of the listener’s ears must be equal to that of the speakers.

4.	Turn Surround Sound Functions off

When the surround sound effect is enabled, it will cause confusion with C3D sound, and make positional sound effect invalid.

Audio Rack Panel

CMI8738 PCI Audio Adapter Layout Notes

- The wires of analog circuits(chip pin64-80) must be wider than 12mil.

- Placing digital signals such as SPDIF IN/OUT(pin86, 98) and TXD/RXD(pin88,89) near the analog signals should be avoided.  However, if these signals have to be adjacent, please place ground between these digital and analog signal wires to isolate noises.

- The whole PCB grounding should be well-organized(The ground must be placed as much as possible.  Also, the ground of both the component and the solder sides should be drilled as much as possible.).

- The grounding under CMI8738 should be well-organized as mentioned above.

- The regulator(78L05) must be placed near the chip as much as possible.

- The chip and the circuits need independent power supply regulators to prevent insufficient currents.

# Text boxes

Rear L/R

CMI-8738/PCI Block Diagram

14.318Mhz

PLL and timing circuit

Analog Mixer

16-bit CODEC

Music Synthesizer HRTF DSP engine

MPU 401 and

GAME port

SPDIF IN and OUT

Legacy audio

SB16™emulator

DMA engine

IRQ control

emulatorll duplex CODECo,nter.0..

A physical speaker

###### PCI BUS

MIC IN

A virtual

speaker

A physical speaker

A virtual speaker

LINE / CD / AUX / PCPSK IN

CMI-8738/PCI AUDIO Specification

PINOUT

MIC AMP

PCI interface

PCI interface

LINE OUT

Earphone buffer

3D Surround

Audio Processing Technology

Audio Processing Technology

Audio Processing Technology

HRTF 3D Positional Audio Technology White-Paper

HRTF 3D Positional Audio Technology White-Paper

HRTF 3D Positional Audio Technology White-Paper

HRTF 3D Positional Audio Technology White-Paper

HRTF 3D Positional Audio Technology White-Paper

HRTF 3D Positional Audio Technology White-Paper

Schematic Circuit

Audio Rack Panel

Two Speakers System :

Four Speakers System :

4 Speakers system Enable

Line-In becomes

Rear Speakers Output

SPDIF Test Report

SPDIF Test Report

Schematic Circuit

POWER ON CONFIGURATION PIN

Schematic Circuit

Schematic Circuit

Schematic Circuit

Schematic Circuit