## Slide 1: Flood risk assessment
Arjen Markus
Deltares
(previous name: WL | delft hydraulics)

## Slide 2: The problem: river floods
Most rivers in the Netherlands surrounded by dikes
Dike breaches are a hazard to be dealt with
Dikes need to be heigh enough and strong enough
This project: comprehensive approach

## Slide 3: Study area (1)

## Slide 4: Study area (2)
Surrounded by Rhine and Meuse
Approximately 2 million people
Several major cities
Agriculture important aspect

## Slide 5: Study area (3)

## Slide 6: River system behaviour
Dike breach can mean: lower water levels downstream
But also: pressure from the land side
Modelling approach:
  Select locations for possible breaches
  Compute the water flow in the rivers and over land
  Estimate casualties and economic damage

## Slide 7: Typical result

## Slide 8: Modelling system

## Slide 9: Modelling system: Scenarios
Monte Carlo simulation: Setting up the scenario
Floods have stochastic properties: maximum flow rate
Dikes vary in strength – parameters known approximately only
Selection:
  Draw parameters for each location
  Relation flow rate – water levels known
  Estimate: dike breach?
Result: 3 x 100 scenarios (for different sets of potential breach locations)

## Slide 10: Modelling system: Hydrodynamics
Fine-grained terrain model (100 x 100 m)
Flood simulated using “standard” curves – known for a range of maximum flood rates
Period to simulate: roughly two weeks to three months
Each simulation takes several days or even weeks to complete

## Slide 11: Modelling system: Estimating victims, damage
Maps of population density and land use
Maps of water levels and flow velocities from hydrodynamic model
GIS-based analysis
Result for each indicated area:
  the number of victims
  Amount of economic damage

## Slide 12: Modelling system: Estimate the risk
Combine the results for all scenarios
Risk is expected number of victims or amount of damage – so multiply with probability of occurrence
Histogram: what is the most likely number of casualties?

## Slide 13: Managing the computations
Different programs run on different sites or computers
Setting up, starting and checking the computations has to be automated:
  A set of 300 scenarios
  Computations take too long
Tcl turns out to be almost perfect for the job

## Slide 14: Preparing the hydrodynamic computation
Copying the (fixed) input files for each computation to a separate directory
Reading the XML file with flood parameters and dike strength parameters
Setting up the timeseries for the flood wave and adjusting various input files
[clock], [string map], [file copy] are the tools here

## Slide 15: Interlude: some code
proc constructTimeseries {begin series} {
set sobekseries {}
set begintime [clock scan $begin]
set offset [lindex $series 0]
foreach {time rate} $series {
set seconds [expr {int(86400*($time-$offset))}]
set datetime [expr {$begintime+$seconds}]
set sobektime [clock format $datetime -format \ "'%Y/%m/%d;%H:%M:%S'"]
lappend sobekseries "$sobektime $rate <"
}
# Trick: using a list suppresses an end-of-line at the end!
return [join $sobekseries \n]
}

## Slide 16: Running the hydrodynamic program
Scheduling the jobs on the Linux cluster
Not too many at a time though (I am not the only user)
Registering the status:
  Has the job started yet?
  Is it finished? If so, successfully?
  Has it been analysed yet?
Small files with specific names flag that status (“running”, “done”, “analysed”)
Script runs via the cron utility – so I keep the system busy

## Slide 17: Running the risk estimation program
Copying the result files from the various directories
Adapting the input files for the program
Running it in batch mode (it was originally a GUI only)
Extracting the relevant information:
set outfile [open "hisssm-samenvatting.txt" w]
set areas {}
foreach file [glob -nocomplain "*-agg.txt"] {
if { $areas == {} } {
set areas [extractAreaDescription $file]
... write header ...
}
set scenid [extractScenarioId $file]
set numbers [extractInformation $file]
puts $outfile "$scenid\t[join $numbers \t]"
}

## Slide 18: Lessons learned
Traceability and monitoring: being able to analyse what went wrong
Automate as much as possible: you may need to repeat the exercise
Can you run the programs in batchmode?

## Slide 19: Formal view: tuplespace
Fill a database with scenarios (here: the file system)
Each record (scenario) goes through various stages
– steps in the chain of individual computations
Ordering between scenarios is irrelevant
Scenarios contain status information

## Slide 20: Formal view: tuplespaces (2)
Each record (scenario) has the following information:
  Scenario ID (directory name containing all the files)
  Status (not started yet, running, finished, analysed)
The scheduler program selects a scenario with the right status and
starts the computational program that belongs to that status.
In terms of tuplespaces: a read operation – the record is taken out
of the database.
When the computational program finishes, a new record is written:
an out operation.

## Slide 21: Formal view: tuplespaces (3)
In this case the stages of the computation are:
  Preparation: from the XML file to a set of input files
  Computation: flood wave and dike breaches
  Analysis: has the computation succeeded?
  If success, estimate casualties and damage
  If not: identify why not?
The tuplespace apprach means the scheduler program needs to know
nothing of the stage of each scenario. It simply scans the directories.

## Slide 22: Formal view: tuplespaces (4)
Compare this to approaches found in literature:
  Formal specification of the computational steps (often via XML)
  The description of the complete computation needs to be analysed and transformed.
  Loops (iterations) are expanded
  The scheduler program keeps track of the stages of the computation.
A loop in this set-up:
Simply write a record with the same status, until the stop criterium
is fulfilled.

## Slide 23: Spin-off
Setting up a series of computations is useful (to me) in other projects too.
For instance: optimising the location of a waste water discharge in a coastal area
Work in progress:
  Various ways of dealing with a series of computations
  Possibility of calibration, not just selecting an alternative
  Flexibility in defining the variations?